 DoMoAct
Based on UNO-R4 Wifi
# Overview

DoMoAct stands for DOMOtica in ACTion

This DoMoAct system can switch on and off ports on a certain time and / or triggered by a sensor. Each port is connected to a GPIO which can be connected to an external relay or controller. As such it can switch any electronic circuit and devices like a garden light, in-house light, pump, electric heating, power outlet, airco etc.

The local time is obtained from an NTP-timeserver and stored in the RTC. Each new day the RTC is updated and the sunrise and sunset times for that day are calculated.

The system is modular so that each port can be set separately to switch On or Off at a certain fixed time or the timing can be depending on the local sunrise or sunset time for that day.

The ports can be assigned to a group. This way you can switch the different ports that switch different lights in the garden, e.g. with just using a group called “garden”. Each group can be set separately to switch On and Off at a certain fixed time or the timing can be depending on the local sunrise or sunset time for that day.

Next to timing setting a sensor can be used to trigger a port. A such one could measure the temperature and if too high, switch on a blower, or measure the water-level and switch on a pump if level is too high or too low. Also motion sensor could be used to switch on light(s) / port(s).

DoMoAct also allows excluding certain days of the week for each port, each group and each sensor.
See chapter “Switch ports and groups” below for more details

The DoMoAct system has both an Serial-interface as well as an Web-interface. The Serial-interface is the primary interface for setup and configuration. The web-interface will allow for limited amount of actions. Is more mend for users with options like manually trigger On/Off the different ports and groups, enable disable (see chapter 10 “web interface” below)

It is build around the UNO-R4 WiFi. See chapter 12 “Hardware”. (see below)

There a number of configuration settings that can be set and changed with a menu. In order to help you plan the solution use the forms that are in appendix I. (see below) or spreadsheet in extras-folder.

About the WEB-INTERFACE: This is a first project for me to create a web-interface. It is working, it is good, but not the best one ever. For sure it could look nicer and easier. Maybe in next versions.
# Disclaimer

This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

Working with high voltage can cause serious equipment and health damage.

THIS IS NOT AN INSTALLATION GUIDE, IT IS GUIDANCE FOR A QUALIFIED PERSON.

MAKE SURE YOU TAKE THE RIGHT SAFETY MEASURES.

IF YOU DO NOT HAVE ENOUGH KNOWLEDGE
OR DO NOT UNDERSTAND… !! STOP !!.

ASK SOMEONE THAT DOES HAVE THE KNOWLEDGE AND/OR QUALIFICATIONS.

# 0. Starting DoMoAct

After reboot DoMoAct first tries to connect to WiFi. If can not connect with WiFiModule it is a fatal error. An error message is on the serial monitor and the onboard led will blink with a frequency of 3 seconds on/off.

Once the module has been connected it will try to connect to the WiFi. The led is off during that time. Once connected the led will be turned on. It will now initialize RTC and connect to the NTP Server to get the correct time. It will try 5 times before failing . If that fails it is a fatal error and the led blink will constant with a frequency of 1 second on/off. If connected the NTP information is stored in the RTC, the sunset/sunrise times will be calculated.

The EEPROM will be read, the sensor channel and sensors (optional) initialized. Next the server will be started and a message will be displayed about the connected network and IP address. The led will now blink 10 times 300ms on/off to indicate we are ready to go.

It will now constant loop to check whether it has to do a time switch or a switch of a port triggered by a sensor.

If the led Matrix is enabled (chapter 11 below), you can get the following messages on the led matrix.
Status	Error
S1	Start to connect to WiFi	E1	SSID or network password missing
S2	Connected to WiFi	E2	WiFi module failed
S3	RTC has been updated by NTP server	E3	NTP connection failed
S4	Starting Server
OK	Ready

# 1. Port, group and sensor channel
The system ports, groups and sensor channels.

A port has a single GPIO assigned which is set active and de-activate at a certain moment. The GPIO output level when active can be set as HIGH or LOW. By default there are 5 ports defined, but it can be changed with EE_NUMPORTS setting.

A group can contain multiple ports. This way you can have different ports/lights in a garden that can be controlled individually, but if you want to switch a number of those ports/lights at the same time, you add those ports to a group. You can also make a group “weekdays” and “weekend” and set different timing for those days. By default there are 5 groups defined, but it can be changed with EE_NUMGROUPS setting.

A sensor channel can switch multiple ports. You add your own code for your sensor to DoMoAct and based on the measured status you can instruct DoMoAct to switch ports On or OFF. By default there are 5 sensor channels defined, but it can be changed that with EE_NUMSENSORS setting.

Ports, groups and sensors channels all have their own individual name up to 20 (EE_NAMELEN) characters.

There is an init-function that set defaults values for each port, each group and each sensor. See appendix L (below) for the default values that will be set. It is a good practice to start with setting the default values with the menu: Main menu: 1 System configuration : 5 Force / set initial setup (see chapter 8 below )

## 1.1 Port settings
Must do :
The port must be assigned to a GPIO. The user makes the choice on which GPIO that is as long as the UNO-R4 WiFi supports it.

The OnHour / OnMinute can be set to a fixed time to switch ON and the OffHour / OffMinute to switch OFF.

Instead of setting a fixed time the port can be set ON based on the sunset time for the day. OnMinute can be set to switch ON minutes earlier. The timing can also be set to switch OFF based on sunrise and the OffMinute can be used to switch OFF minutes later. Next to setting the timing, some weekdays can be excluded as well. See the chapter “Switch ports and groups” below for more details.

The port needs to be enabled in order to be included in the process. See chapter “Enable port, group or sensor channel” (chapter 2 below)

Optional :
After the init-function (below) the GPIO is HIGH when ON, you can change this for each port to be active LOW.

A port after running init-function has a name as PortX (where X is a number). The user can change that to a more logical name for the local situation, like waterfront, barn-light. The name can be up to 20 characters.

Make sure to enable the right working days, by default all days are enabled.

A port can be assigned to different groups. In that case the setting of the port timing is optional as the timing of the group can be used. See the chapter “Switch ports and groups” below for more details.

A port can be assigned to a sensor channel. In that case the setting of the port timing is optional as the sensor can switch the port On or OFF.
## 1.2 Group settings
In case you plan to use a group.

Must do:
There are OnHour / OnMinute to set the fixed time to trigger the assigned ports to switch ON and the OffHour / OffMinute to trigger the assigned ports to switch OFF.

Instead of setting a fixed time the group can be set ON based on the sunset time for the day. OnMinute can be set to switch on minutes earlier. It can also be set to switch based on sunrise and the OffMinute can be used to switch off minutes later. Next to setting the timing, weekdays can be excluded as well. See the chapter “Switch ports and groups” below for more details.

A group must enabled in order to be included in the switching process. See chapter “Enable port, group or sensor channel” (see below)

Optional:
After running the init-function a group will have a default name as GroupX (where X is a number). The user can change that to a more logical name for the local situation, like garden, front. The name can be up to 20 characters.

Make sure to enable the right working days, by default all days are enabled.
## 1.3 Sensor channel settings
In case you plan to use a sensor.

Must do:
One or more ports need to be assigned to a sensor channel. No group can be assigned to a sensor.

A sensor must be enabled in order to be included in the switching process. See chapter “Enable port, group or sensor channel” (see below)

Optional:
After running the init-function a group will have a default name as SensorX (where X is a number). The user can change that to a more logical name for the local situation, like inside temperature, water-level, humidity, motion detector etc. The name can be up to 20 characters.

Make sure to enable the right working days, by default all days are enabled.

# 2. Enable port, group or sensor channel
A port, group or sensor channel must be enabled in order to be included in the switch handling process.

A port can ONLY be enabled if a GPIO number must have been assigned. To be part of the switch process the following condition apply:
- On and OFF times MUST have been set.
- OR sunset and sunrise has been selected. Additional minutes are optional.
- OR the port is assigned to a sensor or group

A group can always be enabled / disabled but in order to be part of the switch process the following condition apply:
- At least one port must have been assigned.
- On and OFF times MUST have been set.
- OR sunset and sunrise has been selected. Additional minutes are optional.

A sensor channel can always be enabled / disabled but in order to be part of the switch process the following conditions apply :
- At least one port must have been assigned.
- Sensor channel included in the user sensor code
A port does not need to have been enabled to assign or while assigned to a group or sensor channel. A group or sensor does not need to be enabled to get a port assigned.

# 3. Switching Ports and groups
## 3.1 Switch based on timing

The time to switch on or off can be set individual for each port and each group with the menu-structure (see chapter 8 below)

The time On/Off can be set as a hard time (e.g. 06.10 or 17.30). The port or group will switch On or Off on the exact time compared to the local stored RTC time. The port or group must have been enabled before.

The time On/Off can also be set relative to sunset or sunrise. This will enable switching the ports and groups On/Off before darkness dawn or after dawn. The sunset and sunrise times are calculated for each day, based on the local Longitude, Latitude and TZ settings provided.

In case of relative to sunrise the port or group will be switched OFF at sunrise time for that day. The off-minutes can be used to set a delay. Setting off-minutes to 15 minutes, the port or group will be switched OFF 15 minutes AFTER the sunrise time.

In case of relative to sunset the port or group will be switched ON at sunset time for that day. The OnMinute can be used to set an earlier start. Setting OnMinute to 15 minutes, the port or group will be switched ON 15 minutes BEFORE the sunset time.

The OnHour and OffHour are NOT used in case of sunset / sunrise.

You can use a mix of sunset & sunrise & fixed hours. So you can use sunset (+ optional OnMinute) to switch on a port/group and use a fixed OffHour/OffMinute to switch the power off.

Apart from the above, for each port or group you can exclude certain days of the week. This can be handy in a weekend where on Saturday / Sunday you don’t want the porch-light to be switched on. Excluding only impacts switching On a port of group. Switching Off will happen on the requested time. By running the init-function all days are enabled.

You can NOT set a different time On/Off for different days on a single port of group. BUT you can assign a port to multiple groups and as such make one group WEEKDAYS and another WEEKEND. Then enable and disable the right weekdays on these groups. That way you can set different times for a port during the week and weekend.

When a port is assigned to a group or sensor, excluding the port on certain days is taken into account and thus NOT switch On that port, although the group or sensor is enabled for that weekday.

In case a port has been assigned to a group, the port will be switched On/Off according to BOTH the GROUP and PORT time setting. Although this is possible the strong advice is to use only the GROUP time settings, but their might a special situation where also a separate port setting is required. Also when a port is assigned to a sensor the switch On/Off is parallel to the time setting.

Port enablement and weekdays days enabled, supersedes either group or sensor settings.

## 3.2 Switch with Sensor channel

Next to timing you can add sensors to DoMoAct to switch On / Off ports.

The code to handle the sensor is yours to include. By default in DoMoAct there is a (disabled) example with a DS1820 temperature sensor code included for reference. For more detail on how to include sensor channel see chapter 9 ( below)

To configure a sensor channel use the menu-structure (see chapter 8 below)

# 4. Time setting

At start-up the system will try to connect over WiFi to an NTP server. It will try 5 times to connect before giving up. If it can not connect the first time around, it is a fatal error.

The information obtained from the NTP server is used to set the on-board RTC. The sunrise and sunset times are calculated for the current day.

After that every night at 01.00 AM an attempt is done to update the RTC from the NTP-Server. This is because the timing on the RTC is not perfect on each board (https://forum.arduino.cc/t/uno-r4-wifi-rtc-runs-fast-by-about-1-second-per-minute/1145956). If that fails, it is not deemed a fatal error and the RTC continues to be source, but maybe get “a little” out of sync. We will try next day again, or you can force with menu option. Also the sunrise and sunset times are calculated for the new day at 01.00 AM.

## 4.1 Daylight Saving Time

DoMoAct handles day light savings for Western Europe or USA in the function DaylightSaving(), in the tab “TimeFunctions”. In DoMoAct.h define DAYLIGHTSAVING as 1 for EU and as 2 for USA.

You can adjust the function to your location in other pars of the world and/or use option 18 in the maintenance menu (see below )to manually toggle the daylight saving.
# 5. Config parameters
There are different configuration settings for different functions.

The different port, group and sensor channel parameter settings are stored in EEPROM and thus maintained in case of power failure or reboot. Each day the EEPROM values are also stored on another place in the EEPROM for backup. With a menu option these can be copied back.

Next to that the EEPROM values can be obtained and stored in a file on a local PC to be reloaded later and restored in the EEPROM.
## 5.1 user Must: WIFI setting
#define SECRET_SSID "*"	// network name
#define SECRET_PASS "*"	// network password
## 5.2 user Must: sunset / sunrise / DaylightSaving setting
float const LATITUDE = 52.3620837035283;// obtain the right values with Google maps
float const LONGITUDE = 4.8911258274758;
#define UTC_OFFSET	1	// difference TZ to UTC
#define DAYLIGHTSAVING 1 // 1 = Western Europe / 2 = USA
## 5.3 user Optional: DoMoAct login
#define DoMoAct_NAME "*"	// DoMoAct name
#define DoMoAct_PASS "*"	// DoMoAct password
#define MIN_PSWD_LENGTH 5	// Minimum length of your passwd to show in webMenu
#define MAX_CH_LENGTH 10 // Max length of either name or password
## 5.4 info: Port parameters
For each port the following parameters can be changed with the menu structure.

struct MyPort{
  uint8_t Gpio;	// GPIO to use
  bool ActiveHigh;	// true : active is HIGH, false : active is low
  char Name[EE_NAMELEN];	// logical name (like backyard, front door )
  uint8_t On_hour;	// Which hours ON
  uint8_t On_minute;	// Which minute ON
  uint8_t Off_hour;	// Which hours OFF
  uint8_t Off_minute;	// Which minute OFF
  bool On_sunset;	// true: use on_minutes to switch ON BEFORE before sunset
  bool Off_sunrise;	// true: use off_minutes to switch OFF AFTER sunrise
  uint8_t Day;	// which Weekdays (bit 0 = Sunday, 1 = ON, 0 = OFF)
  bool Enable;	// true = enabled, false = disabled
  uint8_t Group[EE_NUMGROUPS]; // part of a group

//The following are NOT assigned reserved for future purpose for each port:
  uint8_t future1;	bool futureb1;	float futuref1;
  uint8_t future2;	bool futureb2;	float futuref2;
}

In RAM: bool PortStatus[EE_NUMPORTS];	// on or off

## 5.5 info: Group parameters
For each group the following parameters can be changed with the menu structure.
struct MyGroups {
  char Name[EE_NAMELEN];	// logical name (like garden, house)
  uint8_t On_hour;	// Which hours ON
  uint8_t On_minute;	// Which minute ON
  uint8_t Off_hour;	// Which hours OFF
  uint8_t Off_minute;	// Which minute OFF
  bool On_sunset;	// true: use on_minutes to switch ON BEFORE before sunset
  bool Off_sunrise;	// true: use off_minutes to switch OFF AFTER sunrise:
  uint8_t Day;	// which weekdays (bit 0 = Sunday, 1 = ON, 0 = OFF)
  bool Enable;	// true = enabled, false = disabled
  uint8_t count;	// number of ports member of this group

 // The following are NOT assigned reserved for future purpose for each group:
  uint8_t future1;	bool futureb1;	float futuref1;
  uint8_t future2;	bool futureb2;	float futuref2;
}

In RAM: bool GroupStatus[EE_NUMGROUPS];	// on or off

## 5.6 info: Sensor channel parameters
The structure below is stored in EEPROM:

struct MySensors {
  char Name[EE_NAMELEN];	// logical name (like temperature, water-level, humidity)
  uint8_t Day;	// which weekdays (bit 0 = Sunday, 1 = ON, 0 = OFF)
  bool Enable;	// true = enabled, false = disabled
  uint8_t Ports[EE_NUMPORTS];	// control ports (0xff No port)

 // the following can be used by the sensor program to store
  uint8_t UserInt1;	uint8_t UserInt2;	bool UserBool1;
  bool UserBool2;	float UserFloat1;	float UserFloat2;
}

The following parameters are stored in RAM as they are only valid during the up-time :

byte ChangeSensorStatus[EE_NUMSENSORS];	// need to change on next check
bool SensorStatus[EE_NUMSENSORS];	// on or off

The following defines are used when setting an action on a sensor channel (see below )

#define SENSOR_NOACT 0
#define SENSOR_ON 1
#define SENSOR_OFF 2
#define SENSOR_FLIP 3

## 5.7 info: General information

Next to port, group and sensor information the following is also stored in EEPROM :

Version	indicating the active version
DisplaySwitch	true: Display switch information serial and on Led matrix (menu controlled)
DashBoard[]	holds the ports, groups or sensor on the dashboard. (menu controlled)
WebBackground Which WebBackground to use (menu controlled)
DST daylight saving (automatically set, menu overrule possible)
# 6. Backup / Restore parameters
With the many parameters that can be set, it is important to be able to save and restore the work done.

There are 2 options :
Export the parameters to a serial monitor so the data can be copied to a file on a PC. Import the previous exported data from the serial monitor in DoMoAct.

Backup the parameters into a backup storage space in EEPROM on the UNO-R4 and able to restore them from there.

## 6.1 Backup to PC
With the maintenance menu (below) you can select export the EEPROM data. It will export 5 lines which you save to a file. Each line has a line header like : x: . Here ‘x’ the line serial number. The first line contains the a start header ‘EE’, followed by the length (0x02F4 = 756 bytes). The last byte (0xD0 in this case) is a CRC8 / checksum to make sure all the data is received correctly.

An example of the lines look like:

:1:EE02F48CCDCC8C3F010000000700000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF00000000000000FF01506F727430000000000000000000000000000000FFFFFFFF00007F00FFFFFFFFFFFFFF00000000007F43

:2:8C00007F43FF01506F727431000000000000000000000000000000FFFFFFFF00007F00FFFFFFFFFFFFFF00000000007F4300007F43FF01506F727432000000000000000000000000000000FFFFFFFF00007F00FFFFFFFFFFFFFF00000000007F4300007F43FF01506F727433000000000000000000000000000000FFFFFFFF00007F00FFFFFFFFFFFFFF000000

:3:8C00007F4300007F43FF01506F727434000000000000000000000000000000FFFFFFFF00007F00FFFFFFFFFFFFFF00000000007F4300007F4347726F7570300000000000000000000000000000FFFFFFFF00007F0000FFFF000000000000007F4300007F4347726F7570310000000000000000000000000000FFFFFFFF00007F0000FFFF000000000000007F43

:4:8C00007F4347726F7570320000000000000000000000000000FFFFFFFF00007F0000FFFF000000000000007F4300007F4347726F7570330000000000000000000000000000FFFFFFFF00007F0000FFFF000000000000007F4300007F4347726F7570340000000000000000000000000000FFFFFFFF00007F0000FFFF000000000000007F4300007F4353656E73

:5:8C6F7230000000000000000000000000007F00FFFFFFFFFFFFFF0000000000B8410000904153656E736F7231000000000000000000000000007F00FFFFFFFFFFFFFF00000000007F4300007F4353656E736F7232000000000000000000000000007F00FFFFFFFFFFFFFF00000000007F4300007F4353656E736F7233000000000000000000000000007F00FFFF

:6:38FFFFFFFFFF00000000007F4300007F4353656E736F7234000000000000000000000000007F00FFFFFFFFFFFFFF00000000007F4300007F43D0

Copy & Paste the lines above to a file

This backup could be restored on another UNO-R4 WiFi, making it easier to create duplicates.
## 6.2 Import from PC
With import option you can import each line in order of line serial number. You are asked to provide the line with the correct serial number. The checksum is checked as well as that the imported backup version number is correct. If all correct it will be restored and the imported configuration displayed.

## 6.3 Backup / restore from EEPROM
The Data-EEPROM on an UNO-R4 WiFi can handle in 8 * 1K. The first 1K block is used to store the active parameters. The second 1k block is used to backup the current active parameters. A backup is made each night at 04.00 AM if there was a change in parameters during the day.

From the system maintenance menu (below), you can force making a backup in EEPROM and/or restore the latest backup from the EEPROM. Before a restore is performed the current version number is checked.

# 7. Setting up DoMoAct
Preparing for setting up the DoMoAct system is one of the MOST important tasks for success. Of course you need to decide for the hardware setup first. Get yourself a UNO-R4 Wifi, as we need the WiFi connection to access the NTP server and the web interface. Also decide on the relay / controller board to connect. Find more important information in chapter 12 hardware (below) about that.
Now the real work starts.
Make sure to first do the basics.
In the tab DoMoAct.h you MUST MUST (did I say MUST already ?) define the following:
- The wireless SSID and PASSWORD. We can not connect otherwise.
- Your location longitude, latitude and timezone. Else the sunset and sunrise times will be wrong.
- Choose the Daylight Saving 1 = EU, 2 = USA. In case you are in another part of the world see chapter 4 : timesetting ( above)
Optional you can set in DoMoAct.h a username and password to control access to DoMoAct.
The longitude and latitude can be found with Google Maps. Lookup your place in the world and click the “right-hand mouse” button. It will show an drop-down menu with the longitude and latitude top. Click on that top line with the mouse button. Now it is copied and you can paste it.
How does port looks like ? GPIO, Name ? Timing? Part of Group ? Weekdays ? What does a group look like, timing, name? which ports etc ? Which sensor channel and how configured ? Use the forms that are included (below) to document and plan first. These forms are also available in a spreadsheet in the extras folder. Without doing that you are going to waste a lot of time. It is like preparing meal, preparation is 50% of the job !
Once you have done the planning, the fun part starts : configuring the system :-)
All you have to do is follow the menu structure (below):
- MUST : Initialize the parameters to a known start. (below)
- configure the ports (below)
- configure the groups (below)
- configure sensor channel (below)
- Enable the ports (below)
- Enable the groups (below)
- Enable sensor channel(below)

Now do a dry-run. Test your system. Instead of providing the high voltage you can use a led. Make sure that is a 1K resistor serial to the led. Otherwise use an ohm-meter or just listen to the “click / clack” in case of a relay.
When you think you are done, make a copy of your configuration setting to EEPROM and a file on a PC. (see above)
Also check the TIPS appendix K (below )section in case you have problems.
# 8. Menu structure
With DoMoAct connected on USB you have a serial monitor and can access a menu structure. This menu structure is the primary and only way to configure change, store and backup the configuration parameters.
After the system is started, connected and show the TCP-IP address, press <enter> and you will get the login ONLY IF DoMoAct_NAME and DoMoAct_PASS are set in DoMoAct.h. Else you will get the mainmenu. By default the username and password are NOT set. However if they are set, you can disable (and re-enable again) with system maintenance menu option 15. This can be handy during a complete system configuration as you are logged out often.
 =========== DoMoAct Login ===========
Provide the User name :DoMoAct
Provide the Password : *****
The username and password are set during compile and can not be changed from menu.
If successfully entered the user name password, the main menu will appear.
=========== MAIN menu ===========

1	System configuration
2	System maintenance
3	Manual switch
4	Toggle checking for WebClient & switch during menu
5	Dashboard
6	Sensor menu
9	Done
 Only <enter> is return. (or wait 20 seconds)

As with any input, you have to respond within 20 seconds. If not you will move-up ONE level in the menu-structure. As the main-menu is the top, you will exit the menu. You can always re-enter by just pressing <enter>. This 20 seconds can be changed with INPUTDELAY in the tab DoMoAct.h.

When you are in the menu, the constant checking for client connection, sensors and On/Off switching and checking (optional) local defined sensors is disabled to prevent to many messages and non-expected switching while configuring the system. With option 4 you can toggle that Client connect, sensor checking and checking for switching. The response time will be a bit slower. The setting is NOT saved in EEPROM.
Option 6 your (optional) “Sensor menu” will only appear when enabled by the user see chapter 9.4 (see below)

Pressing 1 <enter> in the mainmenu will give you :

 =========== System configure menu ===========
1	Display current configuration
2	Port configuring
3	Group configuring
4	Sensor channel configuring
5	Force / set initial setup
6	Enable displaying switching
7	Disable displaying switching
8	Done
 Only <enter> is return. (or wait 20 seconds)

Option 2 give the port sub-menu (see below)
Option 3 gives the group sub-menu (see below)
Option 4 gives the Sensor channel sub-menu(see below
Option 5 will give you the initialize menu (see below)
Option 1 will display the all the current configuration settings as it is stored in the structures and EEPROM.
Option 6 will enable the serial output and LED matrix information when a port, group or sensor is switched on or off.
Option 7 will disable the serial output and LED matrix information when a port , group or sensor is switched on or off.
The display switching is stored in EEPROM and enabled by default.

=========== Port configuring menu ===========
1	Display configuration of a port
2	Set port GPIO
3	Toggle switch OnSunset
4	Set OnMinutes
5	Set OnHour
6	Toggle switch OffSunrise
7	Set OffMinutes
8	Set OffHour
9	Toggle Active level
10	Add a port to a group
11	Remove a port from a group
12	Enable a port
13	Disable a port
14	Update port name
15	Set Working days
16	Toggle display updated configuration
17	Clear time setting
18	Display settings
19	Done
 Only <enter> is return. (or wait 20 seconds)

After selecting option 1 to 18, you will be asked to provide a valid port-number. Entering 19 <enter> or only <enter> or wait 20 seconds will bring you back in the system configure menu.

With option 1 will display the current parameters settings for the selected port. You can also provide a ‘*’ and in that case all ports will be displayed.
With option 2 will set the GPIO for the selected port.
With option 3 will enable/disable switching ON at sunset for the selected port.
With option 4 and 5 : you can input the OnMinutes and Onhour for the selected port.
With option 6 will enable/disable switching OFF at sunrise for the selected port.
With option 7 and 8 : you can input the OffMinutes and Offhour for the selected port.
With option 9 you can toggle the active level between LOW or HIGH .
With option 10 and 11 you can add or remove the selected port from a group.
With option 12 and 13 you can enable or disable the selected port.
With option 14 you can change the name for the selected port.

The impact of option 3 to 8 is described in chapter 3 (see above)

With Option 15 you can set the working days for the selected port. A menu will appear
 =========== Set Working Day ===========
1	Sunday	Enabled
2	Monday	Enabled
3	Tuesday	Enabled
4	Wednesday	Enabled
5	Thursday	Enabled
6	Friday	Enabled
7	Saturday	Enabled
8	Ready

Enter number of day to toggle Only <enter> is return. (or wait 20 seconds)
By selecting the number in fron of the day you can toggle between enabled and disabled. After 20 seconds or 8 <enter> or just <enter> the port menu will appear.

With option 16 you can enable to automatically show the updated port information (like option 1)
With option 17 you can clear/reset the timing values to the default. This impacts OnMinutes/Onhour OffMinute/OffHour, disable sunset, disable sunrise. It will also disable the port UNLESS the port is part of a group or sensor.
With option 18 you display the settings in a different format.

 =========== Group configuring menu ===========
1	Display configuration of a group
2	Toggle switch OnSunset
3	Set OnMinutes
4	Set OnHour
5	Toggle switch OffSunrise
6	Set OffMinutes
7	Set OffHour
8	Add a port to a group
9	Remove a port from a group
10	Enable a group
11	Disable a group
12	Update group name
13	Set Working days
14	Toggle display updated configuration
15	Clear time settings
16	Display settings
17	Done
 Only <enter> is return. (or wait 20 seconds)

After selecting option 1 to 16, you will be asked to provide a valid group number. Entering 17 <enter> or only <enter> or wait 20 seconds will bring you back in the system configure menu.

With option 1 will display the current parameters settings for the selected group.You can also provide a ‘*’ and in that case all groups will be displayed.
With option 2 will enable/disable switching ON at sunset for the selected group.
With option 3 and 4 you can input the OnMinutes and Onhour for the selected group.
With option 5 will enable/disable switching OFF at sunrise for the selected group.
With option 6 and 7 you can input the OffMinutes and Offhour for the selected group.
With option 8 and 9 you can add or remove the a port from the selected group.

The impact of option 2 to 7 is described in chapter 3 (see above)

With option 10 and 11 you can enable or disable the selected group.
With option 12 you can change the name for the selected group.
With Option 13 you can set the working days for the selected group. A menu will appear
 =========== Set Working Day ===========
1	Sunday	Enabled
2	Monday	Enabled
3	Tuesday	Enabled
4	Wednesday	Enabled
5	Thursday	Enabled
6	Friday	Enabled
7	Saturday	Enabled
8	Ready

Enter number of day to toggle Only <enter> is return. (or wait 20 seconds)
By selecting the number in front of the day you can toggle between enabled and disabled. After 20 seconds or 8 <enter> or just <enter> the group menu will appear.

With option 14 you can enable to automatically show the updated group information (like option 1)
With option 15 you can clear/reset the timing values to the default. This impacts OnMinutes/Onhour OffMinute/OffHour, disable sunset, disable sunrise.
With option 16 you display the settings differently.

 =========== Sensor channel configuring menu ===========
1	Display configuration of a sensor channel
2	Add a port to a sensor channel
3	Remove a port from a sensor channel
4	Enable a sensor channel
5	Disable a sensor channel
6	Update sensor channel name
7	Set Working days
8	Toggle display updated configuration
9	Display settings
10	Done
 Only <enter> is return. (or wait 20 seconds)

After selecting option 1 to 9, you will be asked to provide a valid sensor channel number. Entering 10 <enter> or only <enter> or wait 20 seconds will bring you back in the system configure menu.

With option 1 will display the current parameters settings for the selected sensor channel.You can also provide a ‘*’ and in that case all sensor channels will be displayed.
With option 2 and 3 you can add or remove the a port from the selected sensor channel.
With option 4 and 5 you can enable or disable the selected sensor channel.
With option 6 you can change the name for the selected sensor channel.
With option 8 you can enable to automatically show the updated sensor channel information (like option 1)
With option 9 you display the settings differently.

With Option 7 you can set the working days for the selected sensor channel. A menu will appear
 =========== Set Working Day ===========
1	Sunday	Enabled
2	Monday	Enabled
3	Tuesday	Enabled
4	Wednesday	Enabled
5	Thursday	Enabled
6	Friday	Enabled
7	Saturday	Enabled
8	Ready

Enter number of day to toggle Only <enter> is return. (or wait 20 seconds)
By selecting the number for the day you can toggle between enabled and disabled. After 20 seconds or 8 <enter> or just <enter> the sensor channel menu will appear.

============ INIT ============
WARNING WARNING WARNING WARNING WARNING WARNING
Current configuration will be overwritten !!!
Are you sure you want to set to initial setup ??
To validate input: 5678 Only <enter> is return. (or wait 20 seconds)

This is an extra question, where you need to provide digits. If not 5678 <enter> or only <enter> or wait 20 seconds will bring you back in the system configure menu. If 5678 <enter> was provided the init-function is called to set the initial values. See appendix L (below)

=========== Maintenance menu ===========
1	Display all configurations
2	Display current time
3	Update time
4	Display sunset/sunrise times
5	Toggle debug message for time functions
6	Toggle debug message for Webfunctions
7	Make a backup to PC
8	Restore a backup from PC
9	Make a backup in EEPROM
10	Restore a backup from EEPROM
11	System health check
12	Display log of recent switches
13	Clear the recent log
14	Restart DoMoAct
15	Toggle login requirement
16	Configure Dashboard
17	Change Web background
18	Manually toggle Daylight Saving
19	Done
 Only <enter> is return. (or wait 20 seconds)

Entering 19 <enter> or just <enter> or wait 20 seconds it will bring you back in the mainmenu.

With option 1 current parameters settings as it is stored in the structures and EEPROM are shown.
With option 2 will display the current RTC time.
With option 3 you can force RTC time to be updated from the NTP server .
With option 4 will display the sunrise and sunset times calculated for the current day.
With option 5 enable/disable display debug information for the time functions. (disabled at start)
With option 6 enable/disable display debug information for the web functions. (disabled at start)

With option 7 you can export the configuration to the serial monitor. (see above)
With option 8 you can import the configuration with the serial monitor. (see above)
With option 9 you copy the configuration TO a backup location in EEPROM. (see above)
With option 10 you copy the configuration FROM the backup location in EEPROM. (see above)
With option 11 you can perform a number of parameter health checks. If there is an error it will it displayed and tried to correct.
With option 12 you can look at a log of a number of recent switches that has happened.
With option 13 you can reset the log.
With option 14 you can restart DoMoAct.
With option 15 you can disable / enable the request to provide Username and Password (if set)
With option 16 you can add/remove ports, groups or sensor channels from the dashboard.(below)
With option 17 you can change the background of the web-interface.
With option 18 you can manually set DaylightSaving, although this is calculated automatically (see above)

=========== Manual switch menu ===========
1	Toggle / Switch a port.
2	Toggle / Switch a group.
3	Toggle / Switch a sensor channel.
4	Done
 Only <enter> is return. (or wait 20 seconds)

Entering 4 <enter> or just <enter> or wait 20 seconds it will bring you back in the main menu.

After selecting 1 the enabled ports will be displayed and you can enter a valid port to toggle. If no port was enabled you get “NO port enabled”. The switch menu is displayed again.

After selecting 2 the enabled groups will be displayed and you can enter a valid group to toggle. If no group was enabled you get “NO group enabled”. The switch menu is displayed again.

After selecting 3 the enabled groups will be displayed and you can enter a valid sensor to toggle. If no sensor was enabled you get “NO sensor enabled”. The switch menu is displayed again.

The DoMoAct has a dashboard where you can add ports, groups or sensor channels. This way you can combine the often used manual switch options in a single overview making it easer for the user.
Below and example:

 =========== Dashboard ===========

0	Sensor	2	Sensor2	Disabled
1	Group	3	Group1	Disabled
2	Port	0	Port0	Enabled	OFF
3	Done
Select entry Only <enter> is return. (or wait 20 seconds)
Entering Done (3 in this case) <enter> or just <enter> or wait 20 seconds it will bring you back in the mainmenu.

If the dasboard is empty OR if option 16 is selected from the maintenance menu, you can change the dashboard content :
 =========== current Dashboard ===========
0	Sensor	2	Sensor2	Disabled
1	Group	3	Group1	Disabled
2	Port	0	Port0	Enabled	OFF

Do you want to 1 = remove, 2 = add or 3 = cancel Only <enter> is return. (or wait 20 seconds)

Entering 3 <enter> or just <enter> or wait 20 seconds it will bring you back in the mainmenu.

When remove is selected it will ask for the line number and remove the port, group or sensor from the Dashboard. It will NOT remove the port, group or sensor itself !!

When selecting add, it will ask whether you want to add a port, group or sensor. After that it will show the options to select to add to the dashboard.
# 9. Including sensor
This chapter is for more advanced programmers as it needs to have changes in the source code on a number of places instead of customization.
=====================================================================
For including a sensor you have to add your own code. Often this code is already part of a tested / working sketch.
## 9.1 Init
Create a routine called Init{SENSORNAME}. Like the included example for the DS1820 in the ‘Sensor_example’ tab : InitDallas(). In here you should place the sensor initialization code, which is often included in setup() of an existing sketch. Add this Initfunction into the ‘InitSensors()’ which is in the tab ‘DoMoAct’ . InitSensors() is always called from setup() in DoMoAct.
## 9.2 Loop
Some sensors (like the DS1820) need to be regularly checked/triggered with code that is normally part of the loop() in your working sketch. In that case create a function, like ‘checkAlarm()’ in the DS1820 example. In here you put the relevant sensor code that was in the loop() of your working sketch. Add that function that needs to be called regularly into the function ‘CheckSensors()’ which is in the tab ‘DoMoAct’. CheckSensors() is always called before checking whether a port or group needs to switch based on timing or sensor channel in DoMoAct.

If your sensor code is using a call-back, then only apply the information from 9.3.
## 9.3 Connect Sensor Channel
Select sensor channel
There are by default 5 sensor channel (0 – 4). You need to select the sensor channel you want to use. In case of the DS1820 example sensor channel 0 is used. With the menu-structure you need to attach the appropriate port(s) to switch, enable the sensor channel and make sure the correct weekdays are enabled. By default all weekdays are enabled on the sensor channel.

Switch the sensor channel
To set a sensor channel, and thus the assigned ports, On or Off all you have to do is include on the right place in your sensor code line like :

ChangeSensorStatus[Sensor channel] = ‘ACTION’;

‘ACTION’ valid options
- SENSOR_ON : switch the sensor channel & ports assigned On
- SENSOR_OFF : switch the sensor channel & ports assigned Off
- SENSOR_FLIP: Flip sensor channel & the ports assigned from Off > On or On > Off

See the DS1820 in the tab sensor_example for more details.

## 9.4 SPECIAL: Include Sensor in menu structure

With some sensors you want to be able make changes or read from the menu-structure as well as store updated parameters in the EEPROM.

Within the DS1820 example it demonstrates how you can do that. Make sure to study in-depth the Serial-menu and Web-menu. To enable that you need to define BOTH EXAMPLESENSOR and USERSENSORMENU in DoMoAct.h as 1.

You can include your own sensor menu the main menu as option 5. (above)

There are important steps:
1. Remove / disable the DS1820 example to make sure it is NOT in the way.
2. Based on the DS1820 change / define you own sensor code asindicated in step 9.1 – 9.4.
3. Replace / change / define your own Serial-menu as part of the sensor code.
4. Replace / change / define your own Webfunctions.

### 9.4.1 Serial-menu interface
Look at the DS1820 example, tab sensor_example, around line 160.
Basically what it does is display information/status and asks questions.
Use the following structure to get an answer:
  int c = GetInput(X);
  if (c < 0) return;

X = the maximum number the user can provide
If the answer is negative, timeout has occurred, or only <enter> and this way you return to the main-menu. Else it is straight forward programming with Serial.print().

### 9.4.2 Web-menu interface
This is a bit more complicated. You might want to read Appendix M (see below )
Then study the user sensor code in the WebFunctions tab upfront. It is demonstrating how to ask different questions, use multiple pages/menus and how to parse the received feedback from the client. If you also want to add your sensor in the web interface.

Tip : enable Webinterface debugging in maintenance menu. (see above)

### 9.4.3 EEPROM usage
Each sensor has 4 variables that can be used by the user sensor program. When the initial init function has be executed in the system configuration menu as option 5. (above)

  uint8_t UserInt1;	integer	intialized as EE_NOTASSIGNED
  uint8_t UserInt2;	integer	intialized as EE_NOTASSIGNED
  bool UserBool1;	bool	initialized as false
  bool UserBool2;	bool	initialized as false
  float UserFloat1;	float	intialized as EE_NOTASSIGNED
  float UserFloat2;	float	intialized as EE_NOTASSIGNED

In the DS1820 example, tab sensor_example, function SetAlarm() around line 285, you find how the EEPROM storage is happening in 2 steps:

Step 1 : Update the EEPROM structure
  EE_DoMoAct.sensors[SensorChannel].UserFloat1 = HighAlarm; //<<<<<<<<<EEPROM usage
  EE_DoMoAct.sensors[SensorChannel].UserFloat2 = LowAlarm; //<<<<<<<<<EEPROM usage

Step 2 : write the updated structure to EEPROM
  // update EEPROM
  EE_WriteToEEprom(); //<<<<<<<<<EEPROM usage

In order to use these restore these values the next time after a restart in the sensor init function (See 9.1) the following code is added (around line 71)

  if (EE_DoMoAct.sensors[SensorChannel].UserFloat1 != EE_NOTASSIGNED)
    HighAlarm = EE_DoMoAct.sensors[SensorChannel].UserFloat1;

  if (EE_DoMoAct.sensors[SensorChannel].UserFloat2 != EE_NOTASSIGNED)
    LowAlarm = EE_DoMoAct.sensors[SensorChannel].UserFloat2;

# 10. Web Interface
After DoMoAct has been started it will show the address to connect like
====================================================
For DoMoAct: open a browser to http://192.168.178.43
====================================================
## General remarks
In the December 2023 version secure web : https is NOT supported available on UNO-R4 WiFi (yet) You have to use http. Some devices might complain, like an smartphone. Maybe in future version this can be supported.
In the December 2023 version GET is used instead of POST. POST is a much better way to get the responds from the client, but it not supported by the UNO-R4 Wifi (yet?). In the current setup the responds is added to the query string (name/value pairs) to the URL. GET has a number of disadvantages, but it is what it is. (https://www.w3schools.com/tags/ref_httpmethods.asp)
Sometimes after a compile and upload the Web connection is not working. Press reset on the UNO-R4 WiFi. Seems to be an issue with the UNO-R4 Wifi.
The web interface is designed to be used by a single client at the time.
When 2 minutes have passed since a last display of a menu, the Web Interface will restart at the beginning. The 2 minutes can be adjusted with WEBMENURESET in DoMoAct.h.
In case you have opened the Serial-menu, no checking of a web-client is done, unless you enable that in main-menu option 4. (see above)
## 10.0 Login menu
This menu is only shown if a username and password are set in DoMoAct.h. If those are defined at “*”, this login menu will be skipped. The username and password are set during compile and can not be changed from menu.

## 10.1 Main menu

After login, or skipping login, this main menu will be displayed. You get 3 options. Select one and click submit.

## 10.2 Manual switch

Selecting Done + submit will bring you back to the main menu.
If you select Toggle switch a port or group or sensor, you will get a request for a valid port or group or sensor.

It will first show a number, the name and whether or not the port or group or sensor is enabled. Last is the current status (On or OFF). Select the number of the port or group or sensor you want to toggle. Only the enabled ports can be switched. Select cancel to return to the manual switch menu.

## 10.3 Configuration menu

Selecting “Done” will bring you back to the main menu.
When selecting a port configuration (or group) configuration the menu looks like

After each menu selection you will now be asked for a valid port (or group). Except for Done, which will bring you back to the system configuration menu.
Display Configuration of a port (or group) will show you the parameters that have been set.
You can enable or disable the port (or group).
You can add or remove a port from a group.

When selecting Sensor Channel configuration the menu looks like

After each menu selection you will now be asked for a valid sensor channel. Except for Done, which will bring you back to the system configuration menu.

Display Configuration of a sensor channel will show you the parameters that have been set.
You can enable or disable a sensor channel.
You can add or remove a port from a sensor channel.
## 10.4 Maintenance menu

Selecting ‘Done’ will bring you back to the main menu.
The current time at refresh, sunrise and sunset are always displayed at the bottom of a menu.
If the refreshed current time is not correct with “Update current time’ you can force DoMoAct to connect to an NTP server and get an updated time.
You can make a backup of the current configuration and / or restore the backup from the EEPROM backup location. By default a backup is made every night if something was changed.
When you select Backup or Restore you will get a new question to confirm you action

Selecting NO or CANCEL will cancel making of the BACKUP or performing a RESTORE.
Restart DoMoAct will cause a reboot of the system. Given the impact you will get a question to confirm the action.

Selecting NO or CANCEL will cancel making reboot / restart.

With Change Background you can select different background themes for the Web menu.
The current background shown in the picture is Scrolling sand.

## 10.5 Dashboard
The often used ports, groups and sensors can be added to a dashboard for manual switch. The dashboard can be defined with the serial-interface menu and can hold 10 items.
# 11. Led Matrix

The led matrix can be enabled with with ‘#define ENABLEMATRIX 1’ in DoMoAct.h.
The font on led matrix is 5x7 (in init_matrix()) as such 2 characters will fit on a standing screen. You can change that to 4x6 and get 3 characters, but I did not like the look.
During startup it will display status information (see Chapter Startup above).
Once started every minute the updated time will be displayed.
When the serial-menu is started the LED matrix will show ‘MN’ and if a client is connected it will show ‘CL’
If DisplaySwitch is enabled in the maintenance menu (see above) the LED matrix will also show the moment a port, group or sensor switched. This option is enabled by default after init-function (see above ). The message will be scrolling and looks like ‘P0 On’
If the DS1820 sensor example is also enabled is will show the temperature in celcius. This is done with a simple call around line 121: MessageMatrix(twoDigits(tempC),M_NO);
TempC	the measured temperature.
twoDigits()	an available function to add a zero in case tempC is below 10.
M_NO	NO scroll (other options M_LEFT, M_RIGHT, M_UP, M_DOWN)

December 2023 : be aware there is an issue with the Led matrix library that I expect tobe solved in the future (https://github.com/arduino/ArduinoCore-renesas/issues/226)

# 12. Hardware
THIS IS NOT AN INSTALLATION GUIDE, IT IS ONLY GUIDANCE FOR A QUALIFIED PERSON. See disclaimer at the start of document

The DoMoAct system is build around the UNO-R4 WiFi. For more information about this board see https://docs.arduino.cc/hardware/uno-r4-wifi

The pins on an UNO-R4 WiFi are 5V / 8mA. That 8mA is very low compared to other boards, e.g. the UNO-R3 was 20mA, but it is what it is. A good article to read about this (https://forum.arduino.cc/t/maximum-pin-current/1145859)

Important that next to 8mA per pin, is the total maximum current of 60mA either sync or positive (https://forum.arduino.cc/t/maximum-pin-current/1145859/42)

So you can NOT directly connect many of the common relay boards as they take easily 30mA- 50mA per relay. There are different options to consider :

1. Use a transistor to control the relay.
2. Use an opto-coupler. This is even better in case you want to switch a heavy load as you get a better separation of the signal.
3. SOME Solid State relays can handle this.
4. If the voltage you want to switch is below 30VDC and not too heavy current, there are a number of MOSFET boards around.

There are MANY good articles on internet on how to connect with low current, some examples :

https://electronics.stackexchange.com/questions/588613/why-is-a-transistor-required-when-connecting-relays-to-an-arduino

https://howtomechatronics.com/tutorials/arduino/control-high-voltage-devices-arduino-relay-tutorial/?utm_content=cmp-true

Or find the right board. Again there are many, but 2 examples:

https://www.amazon.com/ELEGOO-Channel-Optocoupler-Compatible-Raspberry/dp/B09ZQS2JRD/ref=sr_1_2_sspa?crid=2QPD7AFW3SEJX&keywords=elegoo%2Brelay%2Bmodule&qid=1700075067&sprefix=relays%2Belego%2Caps%2C170&sr=8-2-spons&sp_csd=d2lkZ2V0TmFtZT1zcF9hdGY&th=1

https://www.amazon.com/JBtek-Channel-Module-Arduino-Raspberry/dp/B00KTEN3TM/ref=sr_1_10?crid=2QPD7AFW3SEJX&keywords=elegoo+relay+module&qid=1700075067&sprefix=relays+elego%2Caps%2C170&sr=8-10

On most of the relay-boards you not only need to connect the GND and control-pins to the UNO-R4 WiFi, but also the +5V. This +5V is used for the Opto-couplers BUT also to power the relays.
You can source this 5V for the relays from the UNO-R4 Wifi, but often it is better to connect an external wall wart for the relays to improve system stability. If you do so, make sure to also connect the ALSO the GND of that external power supply to the (same) GND pin on the relay-board.

## 11.1 My board

Personally I have the ELEGOO 4 relays.

I have measured that it takes 1.25mA to control the opto-coupler (far below the 8mA). Another 50mA for 1 relay, 88mA for 2 relays, 118mA for 3 relays and 138mA for 4 relays that are activated. Hence when all relays are activated the power supply to VCC must handle 138mA + 5mA = 143mA.

Be aware also that to activate a LOW signal / pull-down needs to be provided for this board.

Simplified schematics for each port on the ELEGOO board

My board and external power
When connecting external 5V wall wart power, remove the jumper on the side and connect the +5V to the upper JD-VCC pin and the 0 / minus / GND to GND as well.
The VCC and GND in the bottom row MUST be connected to the UNO-R4 Wifi in order for the opto-coupler to function. The port-GPIO’s are connected to IN1 / IN2 / IN3 / IN4.

# Appendix A. EEPROM functions
read current values into a structure : void EE_ReadEeprom(bool disp)

write the an update to EEPROM: void EE_WriteToEEprom()

clear all the EEPROM values:	void EE_ClearEeprom()

set initial values for port & group:	void EE_InitEeprom(bool disp, bool SetBack)

enable/disable display switching	EE_SetDisplaySwitch()

Remember webbackground	EE_Set_WebBackGround(int Set)

DayLight Saving Time	EE_Set_DST(int Set)

///////////////////////////////// PORT FUNCTIONS

set GPIO HIGH /LOW active state:	void EE_PT_ActiveLevel(bool s, uint8_t p)

set/ reset Enable of port:	void EE_PT_Enable( bool s , uint8_t p)

update name of port:	void EE_PT_Name(String s, uint8_t p)

update GPIO number of port	void EE_PT_GPIO(int g, uint8_t p)

enable / disable day to trigger :	void EE_PT_SetDay(bool e, uint8_t d, uint8_t p)

set/ reset On_sunset of port:	void EE_PT_Onsunset(bool s, uint8_t p)

update onMinute of port:	void EE_PT_OnMin(int m, uint8_t p)

update OnHour of port:	void EE_PT_OnHour(int h, uint8_t p)

set/ reset Off_sunrise of port:	void EE_PT_Offsunrise(bool s, uint8_t p)

update offminute of port:	void EE_PT_OffMin(int m, uint8_t p)

update OffHour of port:	void EE_PT_OffHour(int h, uint8_t p)

///////////////////////////////// GROUP FUNCTIONS

adding a port to a group:	bool EE_GR_Ports(int g, uint8_t p, bool s)

update name of group:	void EE_GR_Name(String s, uint8_t g)

enable / disable day to trigger	void EE_GR_SetDay(bool e, uint8_t d, uint8_t g)

set/ reset Enable of group:	void EE_GR_Enable(bool s, uint8_t p)

set/ reset On_sunset of group:	void EE_GR_Onsunset(bool s, uint8_t g)

update OnMinute of group:	void EE_GR_OnMin(int m, uint8_t g)

update OnHour of group:	void EE_GR_OnHour(int h, uint8_t g)

set/ reset Off_sunrise of group:	void EE_GR_Offsunrise(bool s, uint8_t g)

update OffMinute of group:	void EE_GR_OffMin(int m, uint8_t g)

update OffHour of group:	void EE_GR_OffHour(int h, uint8_t g)

///////////////////////////////// SENSOR CHANNEL
update ports on sensor channel	bool EE_SN_Ports(int g, uint8_t p, bool s)

enable sensor channel	void EE_SN_Enable( bool s, uint8_t g)

update name sensor channel	void EE_SN_Name(String s, uint8_t g)

set weekdays sensor channel	void EE_SN_SetDay(bool e, uint8_t d, uint8_t g)

///////////////////////////////// BACKUP FUNCTIONS
read values from backup location:	bool EE_ReadBackUpEeprom(bool disp, bool bcheck)

write an update to backup location:	void EE_WriteBackUpToEEprom(bool force)

export data to screen:	void EE_Export()
uint8_t Hto8(char *p)

import earlier exported content:	void EE_Import()
int16_t Getline(uint8_t x)
int16_t Storeline(int16_t ll, uint8_t x)
uint8_t Hto8(char *p)
uint8_t update_crc_8( unsigned char crc, unsigned char val )

///////////////////////////////// DISPLAY FUNCTIONS
display complete information:	void DispObjectInfo()
display a single group info:	void DispGroupInfo(int I, bool d)
display a single port:	void DispPortInfo(int I, bool d)
display a single sensor channel	void DispSensorInfo(int i, bool d)

//////////////////////////////// DASHBOARD FUNTIONS
add or remove from dashboard	bool EE_SetDashboard (int d, int n, bool Set)

# Appendix B. Time functions
initialize Sunsettimes (called once)	void InitSunset()
update Sunset/rise times every day	bool UpdateSunTimes()
read NTP Server update RTC	bool UpdateTime()
String twoDigits(int digits)
unsigned long getNtpTime()
void sendNTPpacket(IPAddress& address)
void alarmCallback()
get part of time from RTC	int GetFromRTC(int v)
determine Daylight saving	void DaylightSaving()
calculate UNIX-time to date	void UnixTimeToDate()

# Appendix C. Switch functions
check each minute for action	void DoSwitchOnOff()
determine the next switch time	void DetermineNextSwitchTime()
switch a port	int SetPort(int p, bool c)
switch all ports in a group	void SwitchPorts(int g, bool SwitchOn)
Check on sensors	void CheckSwitchSensors()
switch all ports on sensor	int SwitchSensor(int se)
# Appendix D. Menu Functions
entry point for menu functions	void StartMenu()
Login menu	bool LoginMenu()
main menu	void MainMenu()
setup Menu top menu	void SysSetupMain()
setup Port	void SysSetupPort(up())
setup Group	void SysSetupGroup()
setup sensor channel	SysSetupSensor()
restore to initial values	void SysSetupInit()
switch ports/groups manual	void ManualSwitch()
system maintenance top menu	void SysMaintenance()
 check different settings	void SysMainHealthCheck()
get input from keyboard	int GetInput(int maxop)
get a valid port group sensor	int8_t GetPortGroupSensor(byte v)
get confirmation on critical action	bool AreYouSure()
check port is part of group or sensor	bool CheckForGroup(int p)
check /set port valid enable	bool PortValidEnable(int p)
set/reset workdays	void HandleWorkDays(byte dev, int8_t n)
display workdays	void DisplayWorkDays(int w, bool n)
update name of port or group	void UpdateName(int h, bool p)

Dashboard menu	void SysDashboard()
display dashboard	int ShowDashboard()
config dashboard	void ConfigDashBoard()
# Appendix E. Sensor Channel functions
Initialize the variables and sensors	void InitSensors()
regularly called to check / update sensors	void CheckSensors()
# Appendix F. Circular buffer functions
Update with switch action	void CB_UpdateBuffer(byte dev, int num, bool c_act )
Add entry to buffer	void CBuf_add_entry(char *p, uint8_t l)
reset buffer	void Cbuf_clear()
Display buffer to serial	void CBuf_disp_entries()

# Appendix G. Web Functions

 Check client connected	void CheckForClient()
Ask for username / password	void LoginWebMenu()
Parse repsondse on login	void LoginWebParse()
Determine which web page	WebMenuSelect()
Determine which parser to use	void WebParseSelect()
Add time info to page	void AddTrailer()
add header to web page	void html_begin(int color)
add end to web page	void html_end()
Start menu web	void MainWebMenu()
Manual switch web menu	void SwitchWebMenu()
Parser for switch menu	void SwitchParse(int s_act)
Config web menu	void ConfigWebMenu()
Port config web menu	void MenuPortConfig()
Group config web menu	void MenuGroupConfig()
Sensor config web menu	void MenuSensorConfig()
Get combination of port, group/sen	void MenuPortAddRemoveGroupSensor(int C_act)
Parser for config web menus	void MenuConfParse(int C_act)
Maintenance web menu	void MaintenanceWebMenu()
Parse for maintenance menu	void MaintenanceParse()
Internal Error page	void MenuError()
Display port, group or sensor page	void WebDisplayConf(int dev)
call back for display port,group	void ParseWebDisplayConf(int m)
Display the weekdays web page	void DisplayWebWorkDays(int w)
Ask double question on critical act	void WebDoubleAsk(int Wact)

Parser for double question	void ParseWebDoubleAsk(int Wact)
Ask for a port, group or sensor	void AskPortGroupSensor(int ask)
Parse a number from feedback	int ParseNumber(int Parsenum)
Parse next menu from feedback	int ParseMenu(int menu)
Main parser feedback	int ParseLine(struct ParseValues *p , int pnum, int detect)
# Appendix H. Led Matrix functions

intialize the Led matrix	void init_matrix()
display a messages on the matrix	void MessageMatrix(String txt, int scroldir)

# Appendix I. Preparation form

In order to help the preparation for configuring the ports, groups and sensors use the templates below. They are also included in the DoMoAct extras-folder as a the spreadsheet.

	PORT	0	1	2	3	4
General	Name
	GPIO	-	-	-	-	-
	Active level	LOW	LOW	LOW	LOW	LOW

Timing	Use sunset	-	-	-	-	-
	on_minutes
	on_hour
	Use Sunrise	-	-	-	-	-
	off_minutes
	off_hour

Workdays	Sunday	X	X	X	X	X
	Monday	X	X	X	X	X
	Tuesday	X	X	X	X	X
	Wednesday	X	X	X	X	X
	Thursday	X	X	X	X	X
	Friday	X	X	X	X	X
	Saturday	X	X	X	X	X

	GROUP	0	1	2	3	4
General	Name

Timing	Use sunset	-	-	-	-	-
	on_minutes
	on_hour
	Use Sunrise	-	-	-	-	-
	off_minutes
	off_hour

Ports	0	-	-	-	-	-
	1	-	-	-	-	-
	2	-	-	-	-	-
	3	-	-	-	-	-
	4	-	-	-	-	-

Workdays	Sunday	X	X	X	X	X
	Monday	X	X	X	X	X
	Tuesday	X	X	X	X	X
	Wednesday	X	X	X	X	X
	Thursday	X	X	X	X	X
	Friday	X	X	X	X	X
	Saturday	X	X	X	X	X

	Sensor channel	0	1	2	3	4
General	Name

Ports	0	-	-	-	-	-
	1	-	-	-	-	-
	2	-	-	-	-	-
	3	-	-	-	-	-
	4	-	-	-	-	-

Workdays	Sunday	X	X	X	X	X
	Monday	X	X	X	X	X
	Tuesday	X	X	X	X	X
	Wednesday	X	X	X	X	X
	Thursday	X	X	X	X	X
	Friday	X	X	X	X	X
	Saturday	X	X	X	X	X

# Appendix J. System parameters

Other then configuration parameters, which can be changed with the menu or MUST be set in order for the system to work correctly, there are system parameters that could be changed before compiling and uploading to the UNO-R4 Wifi.

Defined in DoMoAct.h

////////////////////// PROGRAM parameters ////////////////////////////////////
#define INPUTDELAY 20	// wait max 20 seconds for serial-menu input
#define EE_NUMGROUPS 5	// max number of groups
#define EE_NUMPORTS 5	// max number of ports
#define EE_NUMSENSORS 5 // max number of sensors
#define EE_NUMDASHBOARD 10 // max number on dashboard
#define EE_NAMELEN 20	// max name length port / group / sensor
#define EE_NOTASSIGNED 0xff	// parameters is not assigned
#define EE_IMPORTDELAY 60	// wait max 60 x 500ms = 30 seconds for import
#define TIME_NOTASSIGNED 0xffff // Time is not assigned
#define WEBMENURESET 2 // if more x minutes since last login, reset to main web menu

// circular buffer
#define CB_MAXENTRIES 50 // max log of changes
#define CB_ENTRYSIZE 35 // max character length of each change

int eeAddress = 0;	// Location we want the data to be put.
int BackUp_eeAddress = eeAddress + 0x400 ; // back location on 1K

//////////////// USER OPTIONAL Sensor example and menu ///////////////////////
#define SENSOREXAMPLE 1 // enable sensor example by setting to 1

#ifdef SENSOREXAMPLE == 1 // if sensor example is enabled
#define USERSENSORMENU 1 // if an optional (user defined) menu can also be enabled by setting to 1
#endif

//////////////// USER OPTIONAL enable matrix display ///////////////////////
#define ENABLEMATRIX 1 // enable LED Matrix display set to 1

Defined in TimeFunction

IPAddress timeServer(162, 159, 200, 123); // pool.ntp.org NTP server
#define MAX_RETRY 5	// retry times to connect to NTP server

# Appendix K. tips

Port / Relay issues

- Check that port is enabled.
- Is the right GPIO assigned?
- Is the active level set correct for your board?
- Fixed / hard time settings overrule sunset/sunrise
- If associated to a group, is there a timing conflict ?
- If associated to a sensor, Is timing needed on a port ?

Web connection
- UNO-R4 WiFi does not support secure web, hence only http:// is available.
- UNO-R4 WiFi does not support POST, hence only GET is used. This can cause issues with parsing.
- The server is not always available after a new upload. You need to reset or even remove the power to get it going.
- Web does not respond if in Serial Menu you need to enable checking in the serial main menu.
- To debug Web, enable web debug information in serial maintenance menu.
- The web interface is designed to be used by a single client at the time.
- In case you had provided username / password you need to login. The login parameters can be saved in the browser, saving time to type it all the time.
- If 2 minutes have passed since the last web menu was displayed, the web interface will reset to the starting menu. This timing can be changed before compiling.
Adjusting DoMoAct
A number of variables and parameters can be changed. Be aware the size of the parameters to store in the EEPROM should not exceed 1K. The current version is 756 Bytes

Serial connection
- When connecting over serial, make sure to set for 115200 baudrate
- In case you had provided username / password you need to login to the menu. When you work to make a total configuration you might get logged out often. Constant re-entering username and password can be annoying. In the System maintenance menu you can toggle the need for applying the login information off and on.
# Appendix L. Default setting

When running the Init-function the following parameters are reset and written to the EEPROM:
- All timing on port and groups is removed (onHour, onMinute, sunset, offHour, OffMinute, sunrise)
- GPIO is removed from the ports.
- Active level is set to HIGH.
- All workdays are enabled.
- Ports are removed from groups and sensors.
- Port, group and sensor names are reset.
- Port, group and sensor is disabled.
- DashBoard empty
- Variables are initiatized as EE_NOTASSIGNED or false in case of boolean
- DisplaySwitch = true
- No Day light Saving detection enabled
- WebBackground is set to Starfield.

# Appendix M. High level Webmenu structure
Each menu has a unique number ( e.g. 2 = configuration menu. Each next sub-menu that is called from a menu adds an additional number ( 22 = port configuration) and a next sub menu is adds again a number ( e.g. 221 = display port). The menu page to sent next is stored in ‘MenuWebSel’
Based on the ‘MenuWebSel’ number in the function ‘WebMenuSelect()’ it will determine which menu - page to sent to the client. Once sent the ‘MenuWebSel’ is stored in ‘ParseSelect’.
After sending a menu-page the client is disconnected and DoMoAct will wait for the next connect from the client, assuming this is the responds.
Each complete line of the responds that is received on a menu-page from the client is parsed to detect what responds was sent. Which parser to use is determined in WebParseSelect()’ based on the ParseSelect number. Some menu-responses need a unique parser, others can share the same parser. In the parser routine it is determined which is the next menu-page to send and thus is sets MenuWebSel. On return from the parses the cycle repeats : the menu-page that is defined in MenuWebSel will be send etc.
Parsing
Only the line that start with "GET /DMACT?" is a valid responds-line that is parsed. The other lines are neglected. The information to parse from the valid line can be one of the following:
1. A next menu was selected from the top menu ( e.g. from the main-menu)
2. A number value has been returned ( e.g. a port, group or sensor number)
3. A string value has been returned ( e.g. login on password)
To parse and capture the right information, a structure has been defined that is filled for each menu.
struct ParseValues{
  char lookup[10]; // look up value in line
  int num; // number to return in case of menu or store parsed value
  char val[MAX_CH_LENGTH];// store parsed a char value
};

The “lookup” is a word/needle that is expected in the value responds line. The “lookup” is unique identifier for each potential answer which is defined in the menu-page. In case of :
Select <input type="radio", it is the lookup is defined with “value = xxxx”.
Select <input type="number"> the lookup is defined with “name = ccccc”
Select <input type="password"> the lookup is defined with “name = ccccc”
Select <input type="text"> the lookup is defined with “name = ccccc”

A responds can hold multiple lookup-needles. To support the parsing there are 3 supporting routines explained below.

How does this work with Menu lookup ?

Once you have build the menu-page and used <input type="radio", you will need to fill the structure with the right information. Let’s use the manual switch-menu as example. There are potential 4 options: toggle a port, toggle a group, toggle a sensor or done. If you look at the source you will see that each option has a unique ‘value=’ that is returned, like GET /DMACT?menuL2=MSport HTTP/1.1
You need to define the parsevalues so that each lookup-value is in the parse list. The second entry is the NEXT menu to show (so 11 on the first entry).

ParseValues SwitchWebMenuItems[] {
  {"MSport", 11},
  {"MSgroup",12},
  {"MSsensor",13},
  {"MSdone", WEB_MAIN_MENU}
};

By calling ParseMenu(YY) you will parse the corresponding value for the next menu and it will BOTH store that value (11 in this case) in MenuWebSel variable as well as return this number. If it returns -1 it was not a valid line to parse and the line was ignored. YY is the number for the menu-number to parse. If you look in the function WebParseSelect(), it will call ParseMenu for multiple menus with the correct menu number. As ParseMenu already sets the next menu, no further parsing or setting is needed in this case.
As an example of another usage, in the case of asking for a port, group or sensor number we display status information and ask to select the right entry. That responds is handled by SwitchParse() which is called from WebParseSelect(). Here we call ParseMenu() again to determine the entry selected but now we do further processing of setting a port, group or sensor AND also overrule the MenuWebSel that was set.

How does this work for a Number lookup ?

With a number lookup you have build the menu-page with <input type="number". You can define the minimum and maximum for a number as well as the steps. The bad news is that the formatting is lousy, as you can find on internet. In case you ask for ONE number with ‘name = Select’ and with a line ‘name=Done’ a standard lookup it already in place. Actually that is the only entry available by default for ParseNumber. Notice the the second entry is zero in a line.

ParseValues MenuPGS_Items[] {
  {"Select", 0, ""},
  {"Done", 0, ""}
};

Now look at the UserSensorParse1() as example. It will call ParseNumber(0). If -1 is returned it was NOT a valid line to parse, else it will return the number of matches to lookup values. In case there is a match on the lookup, the number value is stored in corresponding line. As example when the client returns GET /DMACT?Select=25 HTTP/1.1 , ParseNumber will return 1 (as it has ONE match) and in the first line the num (0) is replaced with 25. In case the client selected the line with “name = Done” the “value=xx” defined in the menu-page for that entry will be placed in the second entry. In case you make your own Parse-table you need to add an entry in ParseNumber().

How does this work for a String lookup ?

Let’s use the LoginWebMenu() as example. The username is asked with < input type="text" and the password is asked with <input type="password". The nice thing about the later is that the browser will ask to store the username and password for later usage.
Now you have to build the parse-table based on the “name=xxx” in the lines. Notice the zero setting and empty string.

ParseValues LoginMenuItems[] {
  {"username",0,""},
  {"password",0, ""}
};

In the function LoginWebParse it will call ParseString(WEB_LOGIN_MENU). If it returns -1 it was not a valid line to parse, else it will return the number of matches to lookup values. The string value parsed is stored in the string ‘val’ variable of the corresponding line and the ‘num’ will be set to 1. if the ‘num’ is set to -1 this lookup was NOT detected. In case you make your own Parse-table you need to add an entry in ParseString().